## Slide 1
Payload-Aware Two-Tier UAV Route Planning
System Architecture — Deterministic Pareto Front Construction with Payload-Driven Route Selection
① INPUTS & DATA
Airspace Graph
3-D lattice; nodes filtered by terrain, OSM buildings, no-fly zones and 120 m AGL
Payload Metadata Tags
Fragility 1–5 · Weight 1–3
Urgency 1–3 · Priority 1–5
② TIER 1 — PARETO FRONT CONSTRUCTION
Refreshed periodically per region — not rebuilt per mission
2.1 Edge Cost Assignment
Each edge gets [3-D distance · wind-aware energy · cumulative risk]; risk has 11 terms incl. wind speed & direction
2.2 NAMOA* Search
Vector label search with an admissible heuristic — exact, deterministic front
2.3 Pareto Dominance Pruning
Node-level label dominance and g + h front pruning discard dominated partial routes early
2.4 Pareto Front Storage
Stored front + graph hash — refreshed on expiry or weather drift
③ TIER 2 — PAYLOAD-DRIVEN SELECTION
Runs per mission — sub-second utility scoring, no re-planning
3.1 Payload Metadata Interpreter
Reads Fragility (F), Weight (W), Urgency (U), Priority (P) tags from operator input
3.2 Weight Derivation Formula
w_risk = F·2/Σ w_dist = U·3/Σ w_energy = W·2/Σ — algebraic bridge to Tier 1 objectives
3.3 Normalisation + Utility Scoring
score(pᵢ) = Σ wₖ·(1−ōbjₖ) computed for EVERY stored Pareto point
3.4 argmax Route Selection
Best battery-feasible point (often non-extreme); P ≥ 4 amplifies the dominant weight; weather NO-GO → HOLD
④ MISSION OUTPUT
Mission File Generation
ArduPilot-compatible .waypoints / .plan file from the selected route
Ground-Station Dashboard
Operator enters payload tag once — no manual re-tuning
⑤ UAV CONTROL ↻
MAVLink Upload
Mission file transmitted to the onboard Pixhawk flight controller
Gazebo SITL → Real Flight
ArduPilot SITL validates first; outdoor flight confirms. Route adherence & latency feedback ↻ informs the next refresh
⑥ OUTPUTS
Payload-Matched Optimal Route
Ready-to-Fly Mission File
Reusable Pareto Front — no per-mission re-planning
Non-Extreme Selection for Mixed Payloads
SITL + Flight-Validated Pipeline
payload metadata tags — direct to Tier 2 (bypasses Tier 1)
⑦ PERFORMANCE EVALUATION
Benchmark Scenarios
S1 50n · S2 200n · S3 500n · real-region lattice × 9 wind cases
Pareto Front Quality
Hypervolume (HV) · Pareto Spread / IGD
Tier 2 Selection Evidence
Payload-alignment score, objective ranks, 225-tag sweep, monotonicity
Computation Time
Tier 1 pre-computation vs. MOPSO runtime
Baseline Comparison
vs. A* (×3) · weighted-sum A* · MOPSO (100 particles, 200 iter) — mean ± std over 30 runs
Inputs & Data
Tier 1: Pareto Construction
Tier 2: Payload Selection
Mission Output
Control & Feedback
Evaluation
This architecture separates deterministic Pareto front construction (Tier 1) from instantaneous payload-driven route selection (Tier 2), connected by an explicit algebraic weight-mapping bridge from payload metadata to routing objectives.